## Slide 2: WHMIS 2015
Introduction to WHMIS 2015
Roles, Responsibilities and the Law
Components of the System
  Labels
  SDSs
  Pictograms/Classes/Categories
Workplace-specific Training
Other Sources of Health and Safety Information
Final Test

## Slide 3: Introduction to WHMIS 2015
Many countries have systems for chemical classification and hazard communication
  In Canada, this system is called WHMIS (Workplace Hazardous Materials Information System)
  Canada has aligned with the “Globally Harmonized System for the Classification and Labelling of Chemicals” or GHS
GHS provides harmonized hazard communication worldwide

## Slide 4: Why Learn about WHMIS?
Learning about WHMIS will give you the knowledge to protect yourself and others from the hazards of exposures to chemicals and materials. The topics included are:
The basics of WHMIS,
WHMIS hazard classes and their pictograms,
Labels, and
Safe use and handling tips.

## Slide 5: What is WHMIS 2015?
Main components are:
  Classification – hazardous products fall into hazard classes and categories according to specific rules
  Communication – using labels and Safety Data Sheets (SDSs)
Suppliers are required to attach proper labels to hazardous products, and to provide SDSs to customers.

## Slide 6: Benefits of aligning WHMIS with GHS
Improved, consistent hazard language
Encourages safe transport, handling and use
Promotes better emergency response
Better regulatory efficiency and compliance
Easier trade between countries
Reduced costs
Reduced need for testing and evaluation

## Slide 7: WHMIS 2015
WHMIS ensures that workers are informed and trained about hazardous products
GHS does NOT replace WHMIS. WHMIS has been updated to align with GHS elements. This alignment involves:
  New classification rules and hazard classes
  New hazard pictograms
  New supplier label requirements
  New format for safety data sheets (SDSs)

## Slide 8: WHMIS continues to...
Things that are the same as before:
Workers must be educated and trained in WHMIS
Workplace labels - the labels may look a bit different, and have some new or different information on it
SDSs must be readily available and accessible for workers

## Slide 9: Why is it important to work safely with hazardous products?
Everyone in the workplace has responsibilities
Prevents injuries or illness in the workplace
Some products can cause immediate harm; for others it may not occur until much later when it is too late to change
Unintentional spread of the product to other areas and expose unprotected individuals (e.g., cafeteria, washrooms, or homes)

## Slide 10: Overall Goal
It is important that you know about hazardous products you work with, and know how to protect yourself by working safely.
At the end of this session, you should be able to answer these four important questions:
What are the hazards of the product?
How do I protect yourself from those hazards?
What do I do in case of an emergency?
Where can I get further information?

## Slide 11: Activity
True or False
GHS is a system that promotes clear and consistent hazard communication globally.
WHMIS will no longer exist after GHS is introduced.

## Slide 12: Activity
With WHMIS aligned to GHS there are:
  □ New hazard classes
  □ New symbols
  □ New label and SDS requirements
  □ All of the above
Why is it important to work safely with hazardous products at your workplace?

## Slide 13: Why change?
Before GHS, a product that would be “toxic” under WHMIS in Canada, might have been labelled:
  “harmful” in Europe and Australia
  “moderately toxic” in China
  “hazardous” in New Zealand
  “non-toxic” in India
The biggest advantage of using GHS worldwide is consistency.

## Slide 14: Roles, Responsibilities And The Law

## Slide 15: Workplace Responsibility System (WRS)
Used to be known as the “internal responsibility system (IRS)”.
Foundation: Everyone in workplace (both workers and employers) is responsible for their own health and safety, and for health and safety of others.
Employer and workers work together to identify, assess and resolve health and safety concerns in workplace.

## Slide 16: Worker rights
Saskatchewan was first to protect three rights into OHS legislation for workers.
Worker rights support principles of WRS:
The right to know
The right to participate
The right to refuse

## Slide 17: WHMIS is the Law in Every Workplace
WHMIS is a coordinated system of federal, provincial and territorial laws which apply to every workplace in Canada.
The federal laws do four main things:
  Create WHMIS hazard classes and pictograms
  Describe the rules for classifying products as hazardous products
  Require suppliers to attach labels to chemical protects that are hazardous products
  Require suppliers to provide SDSs to customers.

## Slide 18: WHMIS is the Law in YOUR Workplace
Federal laws are the Hazardous Products Regulations (SOR/2015-17) and the Hazardous Products Act. The Hazardous Products Regulations allow suppliers and employers to apply for trade secret information.
All Canadian jurisdictions, including Saskatchewan, have adopted similar WHMIS regulations for employers. These laws were built on consensus between businesses, labour and government.
In Saskatchewan – WHMIS requirements are found in the Saskatchewan Employment Act, the Occupational Health and Safety Regulations, 1996, and the Occupational Health and Safety (Workplace Hazardous Materials Information System) Regulations.
These Acts and regulations can be found online.

## Slide 19: These regulations require your employer to:
Obtain current SDSs for all WHMIS hazardous products
Make sure current SDSs are made readily available to you.
Ensure that hazardous products are properly labelled.
Educate you about WHMIS.
Provide training on the hazards of WHMIS products in your workplace and on necessary precautions.
Workplace-specific training is the most important part of WHMIS training. Your employer must provide this training.
How your employer may organize site-specific WHMIS 2015 training is an included portion of this course.

## Slide 20: Your Legal Responsibilities
Workers have specific responsibilities in WHMIS. As a worker, you must:
  Take part in your education and training programs.
  Follow safe work procedures.
  Use your WHMIS training.
  Ask your employer where the SDSs are kept. Make sure they are current and readily available to you.
  Inform your employer about any hazards you see in the workplace.
  Inform your employer about deficiencies such as labels on containers that are no longer readable, damaged or lost.

## Slide 21: Suppliers Responsibilities
Suppliers (including manufacturers, importers and distributors) must:
Classify products according to their hazards and the WHMIS criteria.
Provide labels for the product or container.
Provide a current SDS for WHMIS products sold to workplaces.

## Slide 22: Who enforces WHMIS?
WHMIS is enforced by inspectors of Saskatchewan Occupational Health and Safety. Inspectors may:
  Ask you specific questions about your knowledge of any part of the WHMIS program
  Ask you to show them an SDS for the product you work with
  Test your understanding of the content of the SDS or label
  See if you know about the product hazards, safe work practices, or emergency procedures
Inspectors can also ask the manager or supervisor these questions, and about how well the WHMIS program is working.

## Slide 23: Which workplace products are covered by WHMIS?
The WHMIS laws set out rules to determine if a workplace product is hazardous.
The rules are based on properties such as toxicity, flammability and reactivity. If one or more of the rules applies to a product, it is called a hazardous product.
If there are hazardous products in your workplace, you need WHMIS education and training.

## Slide 24: Exclusions
Five categories of products are partially exempt from WHMIS requirements for labels and SDSs, but not WHMIS education and training requirements:
Consumer restricted products (those sold to the general public that are already labelled following the rules of the Canadian Consumer Product Safety Act).
Explosives (as defined by the Explosives Act).
Cosmetics, drugs, food or devices (as defined by the Food and Drugs Act).
Pest control products (for examples pesticides as defined by the Pest Control Products Act).
A nuclear substance, as defined by the Nuclear Safety and Control Act, that is radioactive.

## Slide 25: Exclusions
Four categories of products are fully exempt from all WHMIS requirements:
  Wood and products made of wood
  Manufactured articles
  Tobacco or products made of tobacco
  Products being transported or handled pursuant to the Dangerous Goods Transportation Act, and the Transportation of Dangerous Goods Act.
Hazardous wastes do not require SDSs and WHMIS labels, but the wastes still need to be labelled as hazardous waste and workers need to be educated and trained on safe handling procedures.

## Slide 26: We mention these exclusions because...
You probably have some of these products at your workplace. These products use different labels, symbols or other ways to tell people about their hazardous properties.
If any of these categories of products are used in your workplace, your employer is required to give you information on the hazards and how to work safety with them. You must be provided this information before you start using these products. They can usually get an SDS from the supplier.
There is an example regarding consumer products in the Participant Workbook.

## Slide 27: Why change?
Before GHS, a product that would be “toxic” under WHMIS in Canada, might have been labelled:
  “harmful” in Europe and Australia
  “moderately toxic” in China
  “hazardous” in New Zealand
  “non-toxic” in India
The biggest advantage of using GHS worldwide is consistency.

## Slide 28: Components of the Hazard Classification and Labelling System

## Slide 29: Common Elements
The elements that will be discussed here are:
  Hazard groups, classes, and categories
  Pictograms
  Signal words
  Hazard statements
  Precautionary statements

## Slide 30: Hazard Groups
There are 2 major hazard groups under WHMIS 2015
Physical – flammable liquid, gases under pressure
Health – skin corrosion/irritation, acute toxicity
Within each hazard group, there are hazard classes.
Hazard group ➔ Hazard class ➔ Hazard category

## Slide 31: Hazard Classes
Each hazard group is divided further into hazard classes. Under WHMIS 2015, there are:
  19 physical hazard classes
  12 health hazard classes
  There are also 2 environmental classes from GHS but these classes are not mandatory in Canada.
Hazard group ➔ Hazard class ➔ Hazard category

## Slide 32: Physical Hazard Classes
Explosives*
Flammable gases
Flammable aerosols
Oxidizing gases
Gases under pressure
Flammable liquids
Flammable solids
Self-reactive substances and mixtures
Pyrophoric liquids
Pyrophoric solids
Self-heating substances and mixtures
Substances and mixtures which, in contact with water, emit flammable gas
Oxidizing liquids
Oxidizing solids
Organic peroxides
Corrosive to metals
*WHMIS is not adopting the explosive hazard class. It is covered by other legislation in Canada.

## Slide 33: Health Hazard Classes
Acute toxicity
Skin corrosion/irritation
Serious eye damage/ eye irritation
Respiratory or skin sensitization
Germ cell mutagenicity
Carcinogenicity
Reproductive toxicity
Specific target organ toxicity – single exposure
Specific target organ toxicity – repeated exposure
Aspiration hazard

## Slide 34: Environmental Hazard Classes (GHS defined)
Hazardous to the aquatic environment
Hazardous to the ozone layer
NOTE: It is not mandatory to the environmental hazard classes in Canada, but they are mentioned because you may see these classes identified on labels or SDSs for the products you use.

## Slide 35: WHMIS-defined Hazard Classes
WHMIS legislation defined 6 additional classes. These classes will be used in Canada.
Physical Hazards
Combustible dust
Simple asphyxiants
Pyrophoric gases
Physical Hazards Not Otherwise Classified
Health Hazards
Biohazardous infectious materials
Health Hazards Not Otherwise Classified

## Slide 36: Hazard Categories
A category is a sub-division of a hazard class. A category identifies the degree of hazard within a hazard class.
  Category 1 is the highest level of hazard
  Category 2 in the same class has a lower degree of hazard than Category 1
  And so on.
Sometimes letters are used, A being the highest.
TIP! The numbering system tells you about the level of hazard present.
Hazard group ➔ Hazard class ➔ Hazard category

## Slide 37: Example of Category Ranking
The “Flammable liquid” hazard class has 4 categories defined by flash points (FP) and boiling points (BP)
  Category 1: FP<23 deg C, BP ≤35 deg C
  Category 2: FP<23 deg C, BP ≥35 deg C
  Category 3: FP ≥23 deg C, BP ≤60 deg C
  Category 4: FP>60 deg C, BP ≤93 deg C
Category 1 has the lowest flash point and boiling point, making it the most hazardous category for handling and storage.
! The key point is to know that category 1 has the greatest hazard!

## Slide 38: Hazard Pictograms
Ten hazard pictograms are used
Hazard classes and categories are assigned a pictogram
Each has a distinctive red “square set on point” shape with a solid border (except the biohazardous infectious materials pictogram)
The pictogram represents the potential hazard (e.g., fire, health hazard, corrosion, etc.)

## Slide 39: Pictograms

## Slide 40: Hazard Statements
Hazard statements are brief, standardized sentences that help to describe the degree of the hazard. Examples include:
  Extremely flammable gas
  Contains gas under pressure; may explode if heated
  Fatal if inhaled
  Causes eye irritation
Tip! The wording of the hazard statement helps describe the degree of hazard. For example, “May cause cancer” indicates a higher hazard than “Suspected of causing cancer”.

## Slide 41: Signal Words
There are only two signal words used: “Danger” and “Warning”.
Danger is used for higher hazards.
Note: Some of the lower ranking hazard class/categories do not use a signal word.

## Slide 42: Precautionary Statements
Precautionary statements provide information about how to minimize or prevent exposure including storage, handling, first aid, personal protective equipment, and emergency measures.
Examples include:
  Keep container tightly closed
  Wear protective gloves/protective clothing/eye protection/face protection
  If exposed or concerned: Get medical advice/attention
  Fight fire remotely due to the risk of explosion
  Protect from sunlight

## Slide 43: Putting these elements together
Together, the pictogram, signal word, hazard statement, and the hazard class and category name provide you with information about that hazardous product.

## Slide 44: Supplier Label
Labels alert you to the major hazards and provide some precautions
  Supplier labels will look different than the old WHMIS labels and will have some different information
Labels use all of the elements we just discussed.

## Slide 45: Workplace Label
You may need to make a workplace label.
It should have the:
Product name (matching the SDS)
Safe handling precautions
Reference to the SDS (if available)

## Slide 46: What should a worker do?
Before using a product:
Always check for a label
Read, understand, and follow the instructions on the label (and SDS). Ask your supervisor if you are unsure of any part of its use or storage
Ask for new label if the old one cannot be seen or read properly
Do not use a product that is not labelled
Receive WHMIS education and training

## Slide 47: Activity
Match each term with the example on the label
Product identifier
Pictogram
Signal word
Hazard statement
Precautionary statements
Supplier information

## Slide 48: Activity
Rank the hazard represented by each product based on the pictogram, signal word, and hazard statement. (Use 1 to 4, with 1 being the highest hazard)
___ Flame. Warning. Flammable liquid and vapour
___ (No pictogram). Warning. Combustible liquid
___ Flame. Danger. Extremely flammable liquid and vapour
___ Flame. Danger. Highly flammable liquid and vapour

## Slide 49: Safety Data Sheets (SDSs)

## Slide 50: Why learn about SDSs?
WHMIS requires suppliers to provide their customers with information about the hazards and safe use of their products. The SDS is the main source of this information.
Your employer will receive these SDSDs when they purchase the hazardous products.
Stop and think! Do you know about the hazards of the products you are currently working with? Why is this information important?
IMPORTANT: To complete your WHMIS instruction, your employer must also provide education and training on the hazards and safe work practices for WHMIS products used at your workplace.

## Slide 51: Products
WHMIS establishes rules for classifying products into hazard classes and categories.
Suppliers must attach labels and provide SDSs for those products that meet one or more of the classification criteria according to the Hazardous Products Act and regulations.
When a product meets one or more of the classification criteria, it is known as a hazardous product.

## Slide 52: Safety Data Sheets (SDSs)
SDSs:
Provide more detailed information than the label
Use a standard 16-section format. Information must always be in the same section.
Must be accessible in the workplace (e.g., in a binder or stored electronically)
Will be updated when significant new data becomes available
! It is important to understand the information SDS, and how to find them.

## Slide 53: SDS Sections
Section 1: Identification
Section 2: Hazards Identification
Section 3: Composition/ Information on Ingredients
Section 4: First-Aid Measures
Section 5: Fire-fighting Measures
Section 6: Accidental Release Measures
Section 7: Handling and Storage
Section 8: Exposure Controls/
Personal Protection
Section 9: Physical and Chemical Properties
Section 10: Stability and Reactivity
Section 11: Toxicological Information
Section 12*: Ecological Information
Section 13*: Disposal Considerations
Section 14*: Transport Information
Section 15*: Regulatory Information
Section 16: Other Information
* Content for these sections is not mandatory in Canada

## Slide 54: Who uses SDSs?
SDSs are used by a wide range of people including safety professionals, engineers, emergency responders and doctors.
Some sections of the SDS can be technical to read. If you do not understand the information, ask for help. Ask your supervisor, a health and safety professional, health and safety committee or representative, union or medical professional.

## Slide 55: How to Read and Use the SDS
Use the SDS to help learn about:
  The hazards of the product
  How to work safely with the product
  First-aid measures
  Emergency measures
Tip! Always read the SDSs for the products you use. If unsure, ask your supervisor before handling the product

## Slide 56: 4 Main Purposes of an SDS
Identification – for the product and the supplier
Hazards – health, physical (fire, reactivity), and environmental (if provided)
Prevention – steps you can take to work safely, and reduce or prevent exposure or an emergency
Response – appropriate responses in various situations (e.g., first-aid, fire, accidental release)

## Slide 57: What is hazard analysis?
Hazard analysis is the systematic examination of tasks, process and procedures to identify potential loss exposure.
Approach:
  Inventory tasks
  Identify hazards within each task and assess risks
  Develop plan to eliminate hazards and risks, or reduce the risks associated with hazards
  Write guidelines, procedures/practices and communicate to workers/employers
  Implement, deliver training, follow up

## Slide 58: Hierarchy of Hazard Control
All controls are not created equal. When determining the most effective way to control a hazard, it is valuable to follow the steps shown below:
  Elimination
  Substitution
  Engineering / Design
  Administrative
  Personal Protective Equipment (PPE)

## Slide 59: Activity: Finding your way around an SDS
  What is the product name?
  What are the hazardous ingredients?
  What are the main hazard(s) of this product?
  What are the label elements? (e.g., pictogram, etc.)
  What are the symptoms of breathing this product?
  What are the first-aid measures for eye contact?
  What should be done if the product spills?
  What are the key handling requirements?
  List the recommended protective measure(s).
  What engineering control is recommended?
  What colour is the product?
  Are there any special conditions to avoid?
  Name the incompatible materials.
  What are the routes of exposure?
  List some symptoms of acute (short-term) exposure.

## Slide 60: Multi-hazard products
Many products will have more than one hazard class. For example: Acetone has characteristics that fall into multiple hazard classes:
  flammable liquids
  serious eye damage/eye irritation
  specific target organ toxicity – single exposure
Always review the SDS and label so you are aware of all of the potential hazards, and follow the precautions and advice provided.

## Slide 61: Activity
True or False?
The rules of precedence for information on a label means that sometimes a product will have less protective wording.
It is important to consider other health and safety hazards beyond the hazard pictogram or hazard class/category.
If a product has significant physical hazards such as being corrosive or flammable and steps are taken to control it, then workers do not need to be concerned about health effects.
Notes: Answers: F, T, F

## Slide 62: Hazard Pictogram Summary

## Slide 63: Hazard Pictogram Summary
For each pictogram, we will cover how to recognize the hazard, and some key handling and storage steps you can take.
Education and training for some of these hazard classes may be beyond the scope of this course. Employers must provide this worksite specific training.

## Slide 64: Pictograms and Classes

## Slide 65: General Handling Information
When using any product:
Check the label and SDS for information about the hazards and necessary precautions.
Understand emergency procedures and know what you are to do in an emergency.
Practice good personal hygiene – Wash hands after handling; before smoking, eating or drinking; or before going to the toilet.
If personal protective equipment (PPE) is needed, be sure you have the correct training in its selection, use, fit, and maintenance.

## Slide 66: Exploding Bomb Pictogram
Classes using this symbol:
Explosives (includes (sensitivity to shock, impact and friction; thermal instability; fire and heat hazards) (not mandatory)
Self-reactive substances (Type A and B)
Organic peroxides (Cat. A, and B)
Types of explosive hazards
  Unstable explosives
  Mass explosion
  Severe projection
  Fire, blast or projection
  May explode in fire

## Slide 67: Flame Pictogram
Common classes that use this pictogram:
  Flammable liquids
  Flammable solids
  Flammable aerosols
  Flammable gases
Flammables can ignite easily and burn rapidly
Fires need: fuel, oxygen, and heat (e.g., an ignition source such as a spark)

## Slide 68: Flammable Products
Other potential hazards to consider:
Health hazards
Static electricity
Asphyxiation
Toxic by-products from burning
Flashback
Hot work

## Slide 69: Flammable Products
Handling
Prevent release into the air. Use smallest amounts possible.
Use only in well-ventilated areas.
Eliminate sources of ignition. Keep away from heat. No smoking. No combustibles or incompatibles nearby.
Bonding/grounding, or non-sparking equipment may be required.
Use equipment designed for flammables (e.g., safety cans)
Keep work surfaces clean. Wipe up spills.

## Slide 70: Flammable Products
Storage
Keep away from incompatible materials.
Use equipment designed for flammable storage – e.g., flammable storage fridge, flammable cabinets.
Store in a cool, dry, well-ventilated area, away from direct sunlight and exit paths. Post warning signs.
Keep away from ignition sources such as heat, sparks or open flames. No smoking near flammable storage.
Avoid storing large quantities if possible.
Inspect containers and storage area regularly for signs of leakage or damage.

## Slide 71: Flame over circle Pictogram
3 classes use this pictogram
  Oxidizing gas
  Oxidizing liquids
  Oxidizing solids
The “o” is for oxygen and the flames show that oxidizers are a significant fire hazard.
Oxidizers make fires:
  Burn more intensely
  Burn faster
  Occur easier, sometimes without an ignition source

## Slide 72: Oxidizing Hazards
Other potential hazards to consider:
Health hazards
Incompatible materials

## Slide 73: Oxidizing Products
Handling
Eliminate ignition sources and combustible materials. No smoking.
Keep away from incompatible materials - particularly: greases, lubricants, cleaning solvents, paints, or thinners.
Keep containers tightly closed when not in use.
Avoid spilling product and contaminating the skin or clothing.
Keep work areas clean and tidy. Wipe up spills and keep surfaces clean.

## Slide 74: Oxidizing Products
Storage
Keep away from incompatibles.
Store in a cool, dry, well-ventilated area, away from direct sunlight and exit paths. Post warning signs.
Keep away from ignition sources such as heat, sparks or open flames. No smoking.
Avoid storing large quantities if possible.
Inspect containers and storage area regularly for signs of leakage or damage.
Do not use wooden pallets for storing containers.

## Slide 75: Gas cylinder Pictogram
The 4 hazard categories for Gases under pressure are:
  Compressed gas
  Liquefied gas
  Refrigerated liquefied gas
  Dissolved gas
Other potential hazards to consider:
  Health hazards
  Uncontrolled release of high pressure gas
  Suffocation
  Frostbite

## Slide 76: Gases Under Pressure Products
Handling
Prevent the release of gas into the workplace. Use only in well-ventilated areas. Close all valves when cylinders are not in use. Use the smallest practical cylinder size for a particular job. Use the appropriate regulator.
Keep away from flames and heat sources. No smoking.
Inspect all cylinders and valves for damage and proper labels. Secure cylinders to a wall or rack in an upright position. Leave the cylinder cap in place until the cylinder is secured and ready for use.
Do not drop or bang cylinders against each other.
Avoid direct skin contact with extremely cold liquids or compressed gases escaping from the cylinder.

## Slide 77: Gases Under Pressure Products
Storage
Store compressed gas cylinders in cool, dry, well-ventilated areas, away from incompatible materials and ignition sources. Ensure that the storage temperature does not exceed 52C.
No smoking. Keep away from exits. Post warning signs.
Store compressed gas cylinders in the upright position and securely fastened in place with cylinder valve protection cap in place.
Avoid storing large quantities if possible. Do not keep cylinders longer than the supplier recommends.
Properly and promptly dispose of "empty" or unlabelled cylinders.

## Slide 78: Corrosion Pictogram
This pictogram is used for the physical hazard class: Corrosive to Metals.
  Can attack (corrode) some metals
Also used by two health hazard classes: Skin corrosion/irritation (category 1), and Serious eye damage/eye irritation (category 1)
  Can cause destructive, irreversible damage to the skin and eyes.

## Slide 79: Corrosive Products
Handling
Inspect containers for damage or leaks before handling. Containers can become weak and leak or collapse, spilling the contents.
Do not add water to corrosives – it can cause a violent reaction. If it is absolutely necessary to mix them, slowly add the corrosive to water in small amounts and stir frequently.
Prevent the release of corrosive products. Use only in well-ventilated areas. Use the smallest amount necessary.
Dispense carefully. Keep containers closed when not in use. Use corrosion-resistant equipment. Use resistant containers recommended by the supplier.
Clean up spills promptly and safely.
Avoid direct contact.

## Slide 80: Corrosive Products
Storage
Inspect containers and storage area regularly for signs of leaks or damage. Store in the original, labelled shipping container.
Store the smallest amount possible. Use a “first in/first out” policy.
Store away from incompatible materials, and in a cool, dry, well-ventilated area and out of direct sunlight. Store on plastic trays.
Use storage cabinets designed for corrosives.
Store on shelves closest to floor level (avoid storage above eye level).

## Slide 81: Skull and crossbones Pictogram
These products are fatal, toxic or harmful if inhaled, following skin contact, or if swallowed.
This class represents acute toxic (short-term) effects.

## Slide 82: Acute Toxicity Products
Handling
Avoid release into the air. Use only in well-ventilated areas. Keep containers tightly closed when not in use.
Use smallest amount possible.
Maintain good housekeeping (e.g., clean surfaces, no accumulation of dust).
Inspect containers for damage or leaks before handling.
Never eat, drink, smoke or chew gum in work areas where toxic products are used.
Report spills, leaks or problems with control measures immediately.

## Slide 83: Acute Toxicity Products
Storage
Store in a cool, dry, well-ventilated area, away from direct sunlight and exit paths. Post warning signs.
Keep away from potential ignition sources such as heat, sparks or open flames. No smoking.
Do not stockpile.
Inspect containers and storage area regularly for signs of leaks or damage. Contain spills or leaks by storing in trays made from compatible materials.
Keep containers closed and sealed with tight-fitting lids.
Empty containers may contain hazardous residue.
Store containers at a convenient height for handling, below eye level if possible.

## Slide 84: Health Hazard Pictogram
Pictogram is used for products that cause chronic health effects:
Respiratory or skin sensitization - Respiratory sensitizer – Asthma-like response
Germ cell mutagenicity - Causes changes to cells that can be passed on to offspring.
Carcinogenicity - Can cause cancer
Reproductive toxicity – Impacts on human fertility, development of unborn children
Specific Target Organ Toxicity (STOT) – single exposure - Impact on specific organs or systems following an exposure
STOT – repeated exposure - Impact on specific organs or systems following repeated exposure
Aspiration hazard - When products can enter the lungs and cause serious lung injury

## Slide 85: Health Hazard Products
Handling
Prevent release into the air. Use only in well-ventilated areas. Keep amount used to a minimum.
Avoid repeated or prolonged skin contact with product or with contaminated equipment/surfaces.
Keep work surfaces clean. Wipe up spills. Prevent accumulation of dust or other forms of residue. Prevent contamination of surfaces that unprotected personnel may use.
Inspect all containers for damage or leaks before handling. Keep containers tightly closed when not in use or empty.
Immediately report leaks, spills or failures of the safety equipment (e.g., ventilation system). In the event of a spill or leak, exit the area immediately.

## Slide 86: Health Hazard Products
Storage
Inspect containers and storage area regularly for signs of leaks or damage. Store in the original, labelled shipping container.
Do not stockpile.
Keep cool and dry, in a well-ventilated area and away from direct sunlight. Post warning signs.
Store on shelves closest to floor level (avoid storage above eye level).
Keep containers closed. Keep in closed containers with tight-fitting lids.
Empty containers may contain hazardous residue. Store separately.

## Slide 87: Exclamation Mark
The hazard classes that use this pictogram are:
Respiratory or skin sensitization - Skin sensitizer (Category 1, 1A and 1B) - Causes allergy response by skin (redness, itching, swelling, etc.)
Specific target organ toxicity - Single exposure (Category 3) – e.g., coughing
Skin corrosion/irritation - Skin irritation (Category 2) – e.g., redness or inflammation that is reversible
Serious eye damage/eye irritation - Eye irritation (Category 2 and 2A) – e.g., effects that are reversible within 21 days; also severe skin irritants
Acute toxicity - Oral, Dermal, Inhalation (Category 4) – products that may be harmful if inhaled, swallowed or by skin contact

## Slide 88: Exclamation Mark Products
Handling
Prevent release into the workplace air. Use only in well-ventilated areas.
Avoid repeated or prolonged skin contact with product or with contaminated equipment/surfaces.
Keep work surfaces clean. Wipe up spills. Prevent accumulation of dust or other forms of residue. Prevent contamination of surfaces that unprotected personnel may use.
Inspect all containers for damage or leaks before handling.

## Slide 89: Exclamation Mark Products
Storage
Inspect containers and storage area regularly for signs of leakage or damage. Store in the original, labelled shipping container.
Keep cool and dry, in a well-ventilated area and away from direct sunlight.
Keep containers closed.
Store away from production areas and away from incompatible materials.

## Slide 90: Environment Pictogram
Pictogram is used for substances that can have an effect on the environment. Use of these classes and pictogram is not mandatory in Canada.
Classes
Hazardous to the aquatic environment
Hazardous to the ozone layer

## Slide 91: Environmental Hazard Products
Handling and Storage
Have spill control procedures and equipment ready (e.g., absorbent spill control materials, PPE, etc.). Contain spill quickly with suitable absorbent material.
Dispose of product as hazardous waste properly.
Prevent from contaminating ground water, surface waters and sewer system. Protect floor drains, cover opening to sewer if able to do so and appropriate.
Store in a secure, dry, well-ventilated location. Storage area should have sills which prevent leaks from escaping to sewers.

## Slide 92: Biohazardous Infectious Materials Pictogram
These are materials or organisms (or the toxins they produce) that can cause diseases in people or animals.
  Includes: bacteria, viruses, fungi, parasites
These organisms can live in body tissues and fluids.
Usually found in hospitals, health care facilities, laboratories, veterinary practices or research facilities.
Training for this hazard class is beyond the scope of this course.

## Slide 93: Hazard Class Summary

## Slide 94: Physical hazards
Explosives*
Flammable gases
Flammable aerosols**
Oxidizing gases
Gases under pressure**
Flammable liquids**
Flammable solids
Self-reactive substances
Pyrophoric liquids
Pyrophoric solids
Self-heating substances
Substances that react with water and release flammable gas
Oxidizing liquids**
Oxidizing solids
Organic peroxides
Corrosive to metals**
Combustible dust
Simple asphyxiants
Pyrophoric gases
Physical Hazards not otherwise classified
* Not mandatory
** Are included in participant manual
Notes: Those with * are included in participant manual.

## Slide 95: Health hazards
Acute toxicity**
Skin corrosion/irritation**
Serious eye damage/eye irritation**
Respiratory or skin sensitization
Germ cell mutagenicity
Carcinogenicity**
Reproductive toxicity
Specific Target Organ Toxicity (STOT) – single
STOT – repeated
Aspiration hazard
Biohazardous Infectious Materials
Health Hazards Not Otherwise Classified
** Are included in participant manual

## Slide 96: Environmental Hazards (not mandatory)
Hazardous to the aquatic environment
Hazardous to the ozone layer

## Slide 97: Precautions for all Hazards
Understand ALL of the hazards associated with the product and how to use it safely. Read the label and the SDS thoroughly.
Where possible, use a chemical or product that is less hazardous.
Understand and practice emergency procedures so that you know what to do if it becomes necessary.
Have appropriate fire extinguisher available.

## Slide 98: Physical Hazard Group

## Slide 99: Explosives
These products are not common in most workplaces. Explosives are covered by other legislation in Canada.
Explosives are solids or liquids (or mixtures) which are capable of producing gas at a temperature and pressure and speed which can cause significant damage to the surroundings.
NOTE: Explosive products require very specific handling and storage precautions and are beyond the scope of this course.

## Slide 100: Explosives
Hazard category | Pictogram | Signal word | Hazard statement
Unstable explosives | Exploding bomb | Danger | Unstable explosive
Division 1.1 | Exploding bomb | Danger | Explosive; mass explosion hazard
Division 1.2 | Exploding bomb | Danger | Explosive; severe projection hazard
Division 1.3 | Exploding bomb | Danger | Explosive; fire, blast or projection hazard
Division 1.4 | Exploding bomb | Warning | Fire or projection hazard
Division 1.5 | No pictogram | Danger | May mass explode in fire
Division 1.6 | No label elements are assigned to this class |  | 

## Slide 101: Flammable Gases
These gases readily form flammable mixtures with air can easily catch fire and continue to burn.
Common flammable gases are:
  hydrogen
  acetylene
  propane

## Slide 102: Flammable Gases
Hazard category | Pictogram | Signal word | Hazard statement
1 | Flame | Danger | Extremely flammable gas
2 | No pictogram | Warning | Flammable gas

## Slide 103: Flammable Gases
Key Precautions
Minimize the release into the air. Be aware of dangers such as flash-back.
Use only the smallest amount necessary for the job. Use only in well-ventilated areas.
Remove all ignition sources and combustible materials in the area. No smoking. Practice good housekeeping and keep the area clear of materials that burn.
Use non-sparking ventilation systems and equipment.
Ground and bond cylinders, containers or equipment during transfer operations to prevent buildup of static charge.

## Slide 104: Flammable Aerosols
A flammable aerosol is any product in a non-refillable container that contains a gas under pressure (propellant) that is used to expel or eject the contents through a nozzle.
Examples include:
spray paint,
deodorants
adhesives

## Slide 105: Flammable Aerosols
Hazard category | Pictogram | Signal word | Hazard statement
1 | Flame | Danger | Extremely flammable aerosol Pressurized container: may burst if heated
2 | Flame | Warning | Flammable aerosol Pressurized container: may burst if heated

## Slide 106: Flammable Aerosols
Key Precautions
Store in a cool, dry area. Protect from freezing. Keep out of direct sunlight. Do not store in areas with high temperatures, open flames or other ignition sources.
Minimize the release of flammable aerosol into the air.
Remove combustible materials in the area. No smoking. Be aware of dangers such as flash-back.
Protect aerosol cans from damage such as dropping or punctures.
Inspect the container before each use for signs of damage or corrosion. Do not use if damaged. Use open cans and older cans first.
Use only in well-ventilated areas. Use only the smallest amount necessary for the job. Non-sparking ventilation systems and equipment may be required.

## Slide 107: Oxidizing Gases
Oxidizing gases provide oxygen or contribute to the combustion of other material. Oxidizers do not usually burn by themselves but they will:
  Increase the intensity and speed of a fire by providing more oxygen
  Cause materials that normally do not burn to suddenly catch on fire, sometimes without an ignition source
Examples include:
  nitrogen oxides
  halogen gases such as chlorine and fluorine

## Slide 108: Oxidizing Gases
Hazard category | Pictogram | Signal word | Hazard statement
1 | Flame | Danger | May cause or intensify fire; oxidizer

## Slide 109: Oxidizing Gases
Key Precautions
Minimize release into the air. Use only in well-ventilated areas. Use only the smallest amount necessary for the job.
Keep cool and dry and away from direct sunlight. Store in conditions according to the supplier recommendations.
Remove all ignition sources and combustible materials in the area. No smoking.
Non-sparking ventilation systems and equipment may be necessary.
If the oxidizing gas is also a gas under pressure, follow the additional safety steps required. The label and SDS will provide guidance.

## Slide 110: Gases Under Pressure
There are different types of gases which are stored under pressure in a container.
Compressed gas: entirely a gas at -50C (e.g., oxygen, nitrogen, helium, argon)
Liquefied gas: when packaged under pressure, it is partially liquid at temperatures above -50C (e.g., anhydrous ammonia, chlorine, propane)
Dissolved gas: when packaged under pressure, the gas is dissolved in a liquid phase solvent. (e.g., acetylene)
Refrigerated liquefied gas: when packaged is made partially liquid because of its low temperature (e.g., carbon dioxide, nitrogen, oxygen, liquefied natural gas)

## Slide 111: Gases Under Pressure
Hazard category | Pictogram | Signal word | Hazard statement
Compressed gas | Gas cylinder | Warning | Contains gas under pressure; may explode if heated
Liquefied gas | Gas cylinder | Warning | Contains gas under pressure; may explode if heated
Dissolved gas | Gas cylinder | Warning | Contains gas under pressure; may explode if heated
Refrigerated liquefied gas | Gas cylinder | Warning | Contains refrigerated gas; may cause cryogenic burns or injury

## Slide 112: Gases Under Pressure
Key Precautions
Prevent the release of gas into the workplace. Use only in well-ventilated areas and avoid confined spaces.
Use the smallest possible quantity for the job.
Avoid direct skin contact with extremely cold liquids or compressed gases escaping from the cylinder.
Carefully check all connections before use and periodically during use to be sure they are tight, clean, in good condition and not leaking.

## Slide 113: Gases Under Pressure
Key Precautions: Cylinders
Store compressed gas cylinders in cool, dry, well-ventilated areas, away from incompatible materials and ignition sources.
Do not allow flames to contact cylinders. No smoking.
Secure cylinders to a wall or rack in an upright position. Leave the cylinder cap in place until the cylinder is secured and ready for use.
Use the appropriate regulator.
Inspect cylinders for damage and proper labels. Never open a damaged valve. Ensure cylinders are not giving off odours or hissing sounds.
Do not apply any lubricant, jointing compound or tape to cylinder valves, fittings or regulator threads. Keep dirt, rust, oil or grease away from all cylinders or fittings.
Do not drop or bang cylinders against each other. Move cylinders using a hand truck or cart designed for the purpose.
Report leaks immediately and evacuate if appropriate.

## Slide 114: Gases Under Pressure
Key Precautions: Cryogens
Prevent frostbite - never allow cryogenic liquids to touch skin. Never wear watches, rings or bracelets because they can freeze to exposed skin if splashed by an ultracold gas.
Always wear loose fitting thermally insulated gloves. Wear safety glasses and faceshield when working with a cryogen.
Store cryogen containers in cool, dry, well-ventilated areas, away from incompatible materials and ignition sources.
Ensure that pressure relief valves are working properly and are not frozen shut.
Never tamper with safety devices on vessels, valves or equipment.
Fill containers only with the liquids for which they were designed. Label each container. Fill vessels to the indicated level only. Do not overfill.
Proceed slowly when filling a container or inserting objects into a cryogen to minimize boiling and splashing.

## Slide 115: Flammable Liquids
A fire requires three elements:
fuel,
heat (e.g., ignition source such as a spark), and
air/oxygen
Control the fuel (e.g., the flammable product), keep quantities low, and eliminate sources of ignition.
Flammable liquids are very common.
  4 categories - a category 1 (extremely flammable liquid and vapour) is more hazardous than category 4 (combustible liquid)

## Slide 116: Flammable Liquids
Hazard category | Pictogram | Signal word | Hazard statement
1 | Flame | Danger | Extremely flammable liquid and vapour
2 | Flame | Danger | Highly flammable liquid and vapour
3 | Flame | Warning | Flammable liquid and vapour
4 | No pictogram | Warning | Combustible liquid

## Slide 117: Flammable Liquids
Key Precautions: Handling
Use the smallest amount necessary for the job. Use only in well-ventilated areas. Prevent release into air. Keep containers tightly closed.
Eliminate ignition sources and combustible materials (e.g., oily rags, cardboard boxes). No smoking. Keep work areas clean and tidy.
Keep out of direct sunlight and away from incompatible materials (e.g., strong oxidizers). Do not heat containers.
Ground and bond containers during transfer operations to prevent buildup of static charge.
Have spill control procedures and equipment ready (e.g., absorbent spill control materials, PPE, non-sparking tools, etc.). Avoid using combustible materials (such as paper towels or sawdust).

## Slide 118: Flammable Liquids
Key Precaution: Storage
Use equipment designed for flammable liquid storage. Make sure these devices are labelled and sealed or vented appropriately.
Do not store with other types of chemicals. Check SDS for incompatibles.
In general, avoid storing flammable liquids in basements.
Make sure that storage rooms have properly designed ventilation systems that are regularly maintained.
Keep away from potential ignition sources such as heat, sparks or open flames. No smoking in area. Post warning signs. Never store beside exits or in a way that blocks access.
Inspect storage areas regularly for any deficiencies such as damaged or leaking containers. Provide drip trays and empty them often wherever recurring leakages occur.

## Slide 119: Flammable Solids
A flammable solid is readily combustible, or may cause or contribute to fire through friction
Many flammable solids react with water and cannot be extinguished with dry chemical or carbon dioxide extinguishers.
Examples:
gunpowder,
alkali metals,
magnesium metal, and
sulfur

## Slide 120: Flammable Solids
Hazard category | Pictogram | Signal word | Hazard statement
1 | Flame | Danger | Flammable solid
2 | Flame | Warning | Flammable solid

## Slide 121: Flammable Solids
Key Precautions
Use the smallest amount necessary for the job. Prevent the spread of the solid product into the air. Use only in well-ventilated areas.
Keep away from oxidizers and from heat or ignition sources such as open flames, sparks, radiators, electric power panels. Keep combustible materials away from area where flammable solid is used (e.g., oily rags, cardboard boxes). No smoking.
Promptly and properly clean up spilled product.
Make sure that storage rooms have properly designed ventilation systems that are regularly maintained. Post warning signs. Do not store near exits or in a way that blocks access.

## Slide 122: Self-Reactive Substances and Mixtures
This class covers liquid or solids substances that are sensitive (unstable) with temperature changes and which are able to undergo a strongly exothermic decomposition (e.g., the reaction is fast and gives off a lot of energy – it is potentially explosive) even without the presence of air

## Slide 123: Self-Reactive Substances and Mixtures
Hazard category | Pictogram | Signal word | Hazard statement
Type A | Exploding bomb | Danger | Heating may cause an explosion
Type B | Exploding bomb and Flame | Danger | Heating may cause an explosion
Types C and D | Flame | Danger | Heating may cause a fire
Types E and F | Flame | Warning | Heating may cause a fire
Type G | No label elements assigned |  | 

## Slide 124: Self-Reactive Substances and Mixtures
Key Precautions
Use only in well-ventilated areas. Use the smallest amount necessary for the job. Prevent release into the workplace air. Keep containers closed when not in use.
Follow the supplier's recommendations for handling and storage temperatures.
Keep away from heat and eliminate ignition sources such as sparks or open flames. Keep combustible materials away from area where the product is used (e.g., oily rags, cardboard boxes). No smoking.
Keep work surfaces clean. Prevent accumulation of dust or other residues. Promptly and properly clean up spilled product.
Inspect containers and storage area regularly for signs of leakage or damage. Keep the amount of these products in storage as small as possible.
Have spill control procedures and equipment ready. Avoid using combustible materials (such as paper towels).

## Slide 125: Oxidizing Liquids
Oxidizing liquids are a significant fire hazard. Oxidizers do not usually burn by themselves but they will:
  Increase the intensity and speed of a fire by providing more oxygen.
  Cause materials that normally do not burn to suddenly catch on fire, sometimes without an ignition source
Fires fuelled by oxidizing liquids are tough to extinguish and can spread quickly.
  Examples:
  nitric acid,
  percholoric acid, and
  hypochlorites

## Slide 126: Oxidizing Liquids
Hazard category | Pictogram | Signal word | Hazard statement
1 | Flame over circle | Danger | May cause fire or explosion; strong oxidizer
2 | Flame over circle | Danger | May intensify fire; oxidizer
3 | Flame over circle | Warning | May intensify fire; oxidizer

## Slide 127: Oxidizing Liquids
Key Precautions
Use only in well-ventilated areas. Use the smallest amount necessary for the job. Keep amount in storage as small as possible. Prevent release into the workplace. Keep containers closed when not in use.
Keep away from incompatible materials.
Keep away from heat and eliminate ignition sources such as sparks or open flames. Keep combustible materials away from area where the product is used (e.g., oily rags, cardboard boxes). No smoking.
Keep work surfaces clean. Promptly and properly clean up spilled product. Never return unused product to the original container.
Inspect containers and storage area regularly for signs of leakage or damage. Contain spills or leaks by storing in trays made from compatible materials.
Have spill control procedures and equipment ready. Avoid using combustible materials (such as paper towels) to wipe or clean up spills.
Notes: This hazard class is included in the participant manual.

## Slide 128: Oxidizing Solids
Oxidizing solids are a significant fire hazard. Oxidizers do not usually burn by themselves but they will:
  Increase the intensity and speed of a fire by providing more oxygen
  Cause materials that normally do not burn to suddenly catch on fire, sometimes without an ignition source
Fires fuelled by oxidizing solids are tough to extinguish and can spread quickly.

## Slide 129: Oxidizing Solids
Hazard category | Pictogram | Signal word | Hazard statement
1 | Flame over circle | Danger | May cause fire or explosion; strong oxidizer
2 | Flame over circle | Danger | May intensify fire; oxidizer
3 | Flame over circle | Warning | May intensify fire; oxidizer

## Slide 130: Oxidizing Solids
Key Precautions
Use only in well-ventilated areas. Use the smallest amount necessary for the job. Keep amount in storage as small as possible. Prevent release. Keep containers closed when not in use.
Keep away from incompatible materials.
Keep away from heat and eliminate ignition sources such as sparks or open flames. No smoking.
Keep work surfaces clean. Promptly and properly clean up spilled product. Never return unused product to the original container.
Inspect containers and storage area regularly for signs of leakage or damage. Contain spills or leaks by storing in trays made from compatible materials.
Keep in a cool and dry, in a well-ventilated area and away from direct sunlight and according to any other conditions that may be required.
Have spill control procedures and equipment ready. Avoid using combustible materials (such as paper towels).

## Slide 131: Pyrophoric Liquids
Pyrophoric liquids will ignite spontaneously in air.
Require very careful handling and storage
Extremely reactive toward oxygen (air) and in most cases, water, and must not be exposed to the atmosphere

## Slide 132: Pyrophoric Liquids
Hazard category | Pictogram | Signal word | Hazard statement
1 | Flame | Danger | Catches fire spontaneously if exposed to air

## Slide 133: Pyrophoric Liquids
Key Precautions
Use the smallest amount necessary for the job.
Avoid exposure to air. Pyrophoric liquids can be handled safely in controlled inert atmospheres that exclude air.
Keep away from heat and eliminate ignition sources such as sparks or open flames. Keep combustible materials away from area where the product is used (e.g., oily rags, cardboard boxes). No smoking.
Keep the workspace clear of non‐essential and incompatible materials. Keep work surfaces clean. Promptly and properly clean up spilled product. Never return unused product to the original container.
Keep a container of sodium carbonate (soda ash) or lime or dry sand within arm’s reach when handling pyrophoric products (to smother a reaction with air) or for spills.
Avoid working alone with a pyrophoric product.

## Slide 134: Pyrophoric Solids
Pyrophoric solids will ignite spontaneously in air.
Require very careful handling and storage
Extremely reactive toward oxygen (air) and in most cases, water, and must not be exposed to the atmosphere

## Slide 135: Pyrophoric Solids
Hazard category | Pictogram | Signal word | Hazard statement
1 | Flame | Danger | Catches fire spontaneously if exposed to air

## Slide 136: Pyrophoric Solids
Key Precautions
Use the smallest amount necessary for the job.
Avoid exposure to air. Pyrophoric solids can be handled safely in controlled inert atmospheres that exclude air.
Keep away from heat and eliminate ignition sources such as sparks or open flames. Keep combustible materials away from area where the product is used (e.g., oily rags, cardboard boxes). No smoking.
Keep the workspace clear of non‐essential and incompatible materials. Keep work surfaces clean. Promptly and properly clean up spilled product. Never return unused product to the original container.
Keep a container of sodium carbonate (soda ash) or lime or dry sand within arm’s reach when handling pyrophoric products (to smother a reaction with air) or for spills.
Avoid working alone with a pyrophoric product.

## Slide 137: Self-Heating Substances and Mixtures
Are solids or liquids which, by reacting with air and without added energy, can self-heat and catch fire
  A source of ignition is not required; the product is able to generate enough energy (self-heat) to ignite
Examples:
hay
peat

## Slide 138: Self-Heating Substances and Mixtures
Hazard category | Pictogram | Signal Word | Hazard statement
1 | Flame | Danger | Self-heating; may catch fire
2 | Flame | Warning | Self-heating in large quantities; may catch fire

## Slide 139: Self-Heating Substances and Mixtures
Key Precautions
Use the smallest amount necessary for the job.
Keep away from heat and eliminate ignition sources such as sparks or open flames. Keep combustible materials away from area where the product is used (e.g., oily rags, cardboard boxes). No smoking.
Keep the workspace clear of non-compatible and non‐essential materials.
Keep work surfaces clean. Promptly and properly clean up spilled product. Do not return unused product to the original container.
Ensure that containers are clearly labeled and not damaged.
Contain spills or leaks by storing in trays made from compatible materials.

## Slide 140: Substances and mixtures which, in contact with water, emit flammable gases
These products react with water and release flammable gas.
They are very serious fire hazards.

## Slide 141: Substances which, in contact with water, emit flammable gases
Hazard category | Pictogram | Signal Word | Hazard statement
1 | Flame | Danger | In contact with water releases flammable gases which may ignite spontaneously
2 | Flame | Danger | In contact with water releases flammable gases
3 | Flame | Warning | In contact with water releases flammable gases

## Slide 142
Key Precautions
Use the smallest amount necessary for the job.
Keep away from heat and eliminate ignition sources such as sparks or open flames. Keep combustible materials away from area where the products is used (e.g., oily rags, cardboard boxes). No smoking.
Keep work surfaces clean. Promptly and properly clean up spilled product. Contain spills or leaks by storing in trays made from compatible materials.
Do not return unused product to the original container.
Ensure that containers are clearly labeled and not damaged. Label containers with date opened and disposal date.
Do not reuse empty containers – hazardous residue could remain inside.
Avoid having water (e.g., extinguishers and sprinklers) in areas where water sensitive chemicals are stored.
Have spill control procedures and equipment ready. Avoid using combustible materials (such paper towels).
Substances and mixtures which, in contact with water, emit flammable gases

## Slide 143: Organic Peroxides
Organic peroxides are highly reactive and hazardous products
Tend to ignite easily and burn rapidly. Some can react explosively with heating.
Very unstable and are generally sensitive to light and should be stored in darkness.
Some substances form organic peroxides spontaneously.
Examples of "peroxide-forming products" are diethyl ether, tetrahydrofuran or ethylene glycol dimethyl ether.
Very strict safety steps are required when working with organic peroxides.

## Slide 144: Organic Peroxides
Hazard category | Pictogram | Signal word | Hazard statement
Type A | Exploding bomb | Danger | Heating may cause an explosion
Type B | Exploding bomb and Flame | Danger | Heating may cause a fire or explosion
Types C and D | Flame | Danger | Heating may cause a fire
Types E and F | Flame | Warning | Heating may cause a fire
Type G | No label elements have been assigned |  | 

## Slide 145: Organic Peroxides
Key Precautions
Use only in well-ventilated areas. Use the smallest amount necessary for the job. Minimize release into the air.
Inspect containers and storage area regularly for signs of leakage or damage. Some are sensitive to friction, shock (e.g. dropping or bumping container).
Keep in a cool and dry, in a well-ventilated area and away from direct sunlight and according to any other conditions that may be required. Follow the supplier's recommendations for storage temperatures.
Keep the amount of these products in storage as small as possible.
Check stabilizer/inhibitor levels regularly and replenish as necessary.
Keep away from heat and eliminate ignition sources such as sparks or open flames. Keep combustible materials away from area where the product is used (e.g. oily rags, cardboard boxes). No smoking.
Keep work surfaces clean. Promptly and properly clean up spilled product.

## Slide 146: Corrosive to Metals
Products that are corrosive to metals can damage or destroy metals (such as steel and aluminum)
  Examples: nitric acid, hydrochloric acid and sodium hydroxide solutions
When a corrosive “eats” through a container, the product may spill causing damage, and potential injury or exposure for workers in the area.

## Slide 147: Corrosive to Metals
Hazard category | Pictogram | Signal word | Hazard statement
1 | Corrosion | Warning | May be corrosive to metals

## Slide 148: Corrosive to Metals
Key Precautions
Inspect containers of corrosives for damage or leaks before handling.
Do not add water to corrosive products because this can cause a violent reaction. When mixing, add corrosive to cold water slowly, in small amounts, stirring frequently.
Prevent the release into the workplace. Use only in well-ventilated areas. Use the smallest amount necessary.
Dispense corrosives carefully and keep containers closed when not in use. Use corrosion-resistant equipment.
Clean up any spills promptly and safely.
Use only the types of resistant containers recommended by the supplier.
Avoid direct contact.
Store away from incompatible materials and in a cool, dry, well-ventilated area, and out of direct sunlight.

## Slide 149: Combustible Dusts
Combustible dust is defined means “a mixture or substance that is in the form of finely divided solid particles that, upon ignition, is liable to catch fire or explode when dispersed in air”.
Examples:
  Most solid organic materials (such as sugar, flour, grain, wood, etc.)
  Many metals
  Some nonmetallic inorganic materials
Hazard category | Pictogram | Signal word | Hazard statement
1 | No pictogram | Warning | May form combustible dust concentration in air

## Slide 150: Combustible Dusts
Key Precautions
Where possible, avoid horizontal surfaces (such as window ledges, beams, light fittings, etc.) where dust can accumulate.
Do not use brooms or compressed air hoses to clean surfaces.
Remove open flames, sparks, friction, heat sources and other sources of ignition.
Inspect for dust at regular intervals.
Use proper equipment and techniques when cleaning dust. Care must be taken to minimize dust clouds, and only use vacuums approved for dust collection.

## Slide 151: Simple Asphyxiants
Asphyxiants are gases that are able to displace (replace) oxygen in the air. Death from suffocation can occur.
Examples include carbon dioxide and carbon monoxide.
Hazard category | Pictogram | Signal word | Hazard statement
1 | No pictogram | Warning | May displace oxygen and cause rapid suffocation

## Slide 152: Pyrophoric Gases
Pyrophoric gases will ignite spontaneously in air.
Examples are silane, diborane, and phosphine.
Hazard category | Pictogram | Signal word | Hazard statement
1 | Flame | Danger | Catches fire spontaneously if exposed to air

## Slide 153: Pyrophoric Gases
Key Precautions
Use the smallest amount necessary for the job.
Keep away from heat and eliminate ignition sources such as sparks or open flames. Keep combustible materials away from area where the product is used (e.g., oily rags, cardboard boxes). No smoking.
Avoid working alone with pyrophoric products.

## Slide 154: Physical Hazards Not Otherwise Classified (PHNOC)
Characteristics of products placed in this class will vary. Always read the label and SDS for information for specific instructions.
Hazard category | Pictogram | Signal word | Hazard statement
1 | As applicable to the hazard | Danger | Applicable wording for the hazard

## Slide 155: Health Hazard Group

## Slide 156: Acute Toxicity
The acute toxicity class uses two pictograms to indicate chemicals that can cause adverse health effects.
Acute toxicity hazards can cause effects if they:
  are inhaled (inhalation),
  come in contact with the skin (dermal), or
  are swallowed (oral)

## Slide 157: Acute Toxicity
Hazard category | Pictogram | Signal word | Hazard statement
1 | Skull and crossbones | Danger | Fatal if swallowed (oral) Fatal in contact with skin (dermal) Fatal if inhaled (gas, vapour, dust, mist)
2 | Skull and crossbones | Danger | Fatal if swallowed (oral) Fatal in contact with skin (dermal) Fatal if inhaled (gas, vapour, dust, mist)
3 | Skull and crossbones | Danger | Toxic if swallowed (oral) Toxic in contact with skin (dermal) Toxic if inhaled (gas, vapour, dust, mist)
4 | Exclamation mark | Warning | Harmful if swallowed (oral) Harmful in contact with skin (dermal) Harmful if inhaled (gas, vapour, dust, mist)

## Slide 158: Acute Toxicity
Key Precautions
Avoid generating or releasing product into the air. Keep containers tightly closed when not in use. Use only in well-ventilated areas.
Maintain good housekeeping (e.g. clean surfaces, no accumulation of dust).
Store in the original, labelled, shipping container. Inspect containers and storage area regularly for signs of leakage or damage.
Store containers of product in a secure location, away from process and production areas and away from incompatible materials.
Empty containers may contain hazardous residue. Store separately. Keep closed.
Never eat, drink, smoke or chew gum in work areas where products are used.
Be aware of the typical symptoms of an overexposure. Any signs of illness should be reported immediately to the supervisor.

## Slide 159: Skin Corrosion / Irritation
This hazard class covers products that are corrosive or irritating to skin.
Category 1A to 1C: cause irreversible damage to skin
  Examples are strong acids and bases
Category 2: irritants and can cause reversible skin damage.

## Slide 160: Skin Corrosion / Irritation
Hazard category | Pictogram | Signal word | Hazard statement
Skin corrosion,1A to 1C | Corrosion | Danger | Causes severe skin burns and eye damage
Skin irritation, 2 | Exclamation mark | Warning | Causes skin irritation

## Slide 161: Skin Corrosion / Irritation
Key Precautions
Prevent uncontrolled release into the air. Use only in well-ventilated areas. Use the smallest amount necessary.
Avoid direct contact. Avoid repeated or prolonged skin contact with product or with contaminated surfaces. Wear appropriate PPE.
Inspect containers for damage or leaks before handling. Open containers slowly and carefully. Dispense carefully and keep containers closed when not in use. Clean up any spills or dust buildup promptly and safely.
Store away from incompatible materials and in a cool, dry, well-ventilated area and out of direct sunlight.
Know where the closest eyewash station and safety shower are located and how to use them. Call immediately for emergency medical assistance.

## Slide 162: Serious Eye Damage / Eye Irritation
There are three categories
Category 1: cause irreversible damage to the eyes
Category 2A: moderately irritating to the eyes but the damage is reversible
Category 2B: mild irritants which cause minor and reversible damage to the eyes

## Slide 163: Serious Eye Damage / Eye Irritation
Hazard category | Pictogram | Signal word | Hazard statement
1 | Corrosion | Danger | Causes serious eye damage
2A | Exclamation mark | Warning | Causes serious eye irritation
2B | No pictogram | Warning | Causes eye irritation

## Slide 164: Serious Eye Damage / Eye Irritation
Key Precautions
Prevent uncontrolled release into the air.
Use only in well-ventilated areas. Use the smallest amount necessary.
Inspect containers for damage or leaks before handling.
Wear appropriate PPE.
Open containers slowly and carefully. Dispense carefully and keep containers closed when not in use. Clean up any spills or dust buildup promptly and safely.
Store away from incompatible materials and in a cool, dry, well-ventilated area and out of direct sunlight.
Know where the closest eyewash station and safety shower are located and how to use them. Call immediately for emergency medical assistance.

## Slide 165: Respiratory or Skin Sensitization: Respiratory sensitizer
Sensitization is an allergic response by the body’s immune system. Sensitization is a “whole-body” allergic response.
Responses to sensitizers vary. Some people will never be sensitized, others may become sensitized after a single exposure. Once a person has been sensitized, their body will respond to that sensitizer very quickly when exposed to it again.
  Examples: latex, many metals, various acrylates, isocyanates (such as HDI, TDI, MDI), and styrene.

## Slide 166
Hazard category | Pictogram | Signal word | Hazard statement
Respiratory sensitizer 1, 1A, 1B | Health hazard | Danger | May cause allergy or asthmatic symptoms or breathing difficulties if inhaled
Respiratory or Skin Sensitization: Respiratory sensitizer

## Slide 167: Respiratory or Skin Sensitization: Respiratory sensitizer
Key Precautions
Prevent uncontrolled release into the air. Use only in well-ventilated areas. Use the smallest amount necessary.
Unprotected persons should avoid all contact. Use appropriate engineering controls.
Be aware of the typical symptoms of an allergic reaction. Report any signs of illness or exposure concerns to your supervisor immediately.
Wear appropriate PPE.
Report leaks, spills or ventilation failures immediately. Put on a suitable respirator immediately if a respiratory sensitizer is released into the workplace.
Open containers slowly and carefully. Dispense carefully and keep containers closed when not in use. Clean up any spills or dust buildup promptly and safely.

## Slide 168: Respiratory or Skin Sensitization: Skin sensitizer
Sensitization is an allergic response by the body’s immune system. Sensitization is a “whole-body” allergic response.
Responses to sensitizers vary. Some people will never be sensitized, others may become sensitized after a single exposure. Once a person has been sensitized, their body will respond to that sensitizer very quickly when exposed to it again.
  Examples include: latex, methyl methacrylate, toluene diisocyanate (TDI)

## Slide 169: Respiratory or Skin Sensitization: Skin sensitizer
Hazard category | Pictogram | Signal word | Hazard statement
Skin sensitizer 1, 1A, 1B | Exclamation mark | Warning | May cause an allergic skin reaction

## Slide 170: Respiratory or Skin Sensitization: Skin sensitizer
Key Precautions
Prevent uncontrolled release into the air. Closed handling systems can prevent the release of the products. Use only in well-ventilated areas. Use the smallest amount necessary.
Be aware of the typical symptoms of an allergic reaction. Report any signs of illness or exposure concerns to your supervisor immediately.
Wear appropriate PPE.
Open containers slowly and carefully. Dispense carefully and keep containers closed when not in use. Clean up any spills or dust buildup promptly and safely.

## Slide 171: Germ Cell Mutagenicity
This hazard class defines a genetic mutation as a permanent change to the genetic material that is passed on to children.
  Germ cells are the specialized cells involved in reproduction - they carry the genetic material that is passed on to future generations. Damage to the germ cells can have an impact on the genetic information passed to an unborn child and may result in illness or malformations.
Read the SDS carefully to make sure that you understand the nature of the hazard.

## Slide 172: Germ Cell Mutagenicity
Hazard category | Pictogram | Signal word | Hazard statement
1, 1A, 1B | Health hazard | Danger | May cause genetic defects
2 | Health hazard | Warning | Suspected of causing genetic effects

## Slide 173: Germ Cell Mutagenicity
Key Precautions
Prevent uncontrolled release into the air. Use appropriate engineering controls. Closed handling systems can prevent the release of the product. Use only in well-ventilated areas. Use the smallest amount necessary.
Restrict access to areas where these products are used. Post warning signs.
Wear appropriate PPE.
Inspect containers for damage or leaks before handling. Open containers slowly and carefully. Dispense carefully and keep containers closed when not in use.
Clean up any spills or dust buildup promptly and safely.
Report leaks, spills or ventilation failures immediately.
Store away from incompatible materials and in a cool, dry, well-ventilated area and out of direct sunlight.

## Slide 174: Carcinogenicity
Agents that cause cancer, or increase the risk of cancer, are called carcinogens
Carcinogens can enter the body through the skin, lungs, or the digestive system.
  Examples: ultraviolet light (skin cancer), solvents such as benzene (leukemia), carbon tetrachloride (liver cancer)
The latency (time) for cancer to develop can vary. It may range from 5 years up to 20 years or more.
There is no known “safe” level. People react differently. Because of this variation, exposure should always be avoided or kept to the lowest level possible.

## Slide 175: Carcinogenicity
Hazard category | Pictogram | Signal word | Hazard statement
1, 1A, 1B | Health hazard | Danger | May cause cancer
2 | Health hazard | Warning | Suspected of causing cancer

## Slide 176: Carcinogenicity
Key Precautions
Prevent uncontrolled release into the air. Use appropriate engineering controls. Closed handling systems can prevent the release of the product. Use only in well-ventilated areas. Use the smallest amount necessary.
Restrict access to areas where these products are used. Post warning signs.
Wear appropriate PPE.
Inspect containers for damage or leaks before handling. Open containers slowly and carefully. Dispense carefully and keep containers closed when not in use.
Clean up any spills or dust buildup promptly and safely.
Report leaks, spills or ventilation failures immediately.
Store away from incompatible materials and in a cool, dry, well-ventilated area and out of direct sunlight.

## Slide 177: Reproductive Toxicity
This hazard class includes products that may damage or are suspected of damaging fertility or the unborn child (baby).
Note: There is an additional category which includes products that may cause harm to breast-fed children.

## Slide 178: Reproductive Toxicity
Hazard category | Pictogram | Signal word | Hazard statement
1, 1A, 1B | Health hazard | Danger | May damage fertility or the unborn child
2 | Health hazard | Warning | Suspected of damaging fertility or the unborn child
Additional Category: Effects on or via lactation | No pictogram | No signal word | May cause harm to breast-fed children

## Slide 179: Reproductive Toxicity
Key Precautions
Prevent uncontrolled release into the air. Use appropriate engineering controls. Use only in well-ventilated areas. Use the smallest amount necessary.
Restrict access to areas where these products are used. Post warning signs.
Wear appropriate PPE.
Inspect containers for damage or leaks before handling. Open containers slowly and carefully. Dispense carefully and keep containers closed when not in use.
Clean up any spills or dust buildup promptly and safely.
Report leaks, spills or ventilation failures immediately.
Store away from incompatible materials and in a cool, dry, well-ventilated area and out of direct sunlight.

## Slide 180: Specific Target Organ Toxicity - Single
This class includes products where a single exposure can cause significant, non-lethal damage to organs.
  Target organs can include the liver (caused by hepatoxins), kidneys (caused by nephrotoxins), the nervous system (caused by neurotoxins) as well as the blood, lungs or skin.
In addition, products that may cause respiratory tract irritation and/or drowsiness or dizziness are covered in this class.

## Slide 181: Specific Target Organ Toxicity - Single
Hazard category | Pictogram | Signal word | Hazard statement
1 | Health hazard | Danger | Causes damage to organs
2 | Health hazard | Warning | May cause damage to organs
3 | Exclamation mark | Warning | May cause respiratory irritation or May cause drowsiness or dizziness

## Slide 182: Specific Target Organ Toxicity - Single
Key Precautions
Prevent uncontrolled release into the air. Use appropriate engineering controls. Use only in well-ventilated areas. Use the smallest amount necessary.
Wear appropriate PPE.
Inspect containers for damage or leaks before handling. Open containers slowly and carefully. Dispense carefully and keep containers closed when not in use.
Clean up any spills or dust buildup promptly and safely.
Report leaks, spills or ventilation failures immediately.
Store away from incompatible materials and in a cool, dry, well-ventilated area and out of direct sunlight.

## Slide 183: Specific Target Organ Toxicity - Repeated
This class includes products where repeated exposure can cause damage to organs or body systems
  Target organs can include the liver (caused by hepatoxins), kidneys (caused by nephrotoxins), the nervous system (caused by neurotoxins), as well as the blood, lungs or skin

## Slide 184: Specific Target Organ Toxicity - Repeated
Hazard category | Pictogram | Signal word | Hazard statement
1 | Health hazard | Danger | Causes damage to organs <...> through prolonged or repeated exposure
2 | Health hazard | Warning | May cause damage to organs <...> through prolonged or repeated exposure

## Slide 185: Specific Target Organ Toxicity - Repeated
Key Precautions
Prevent uncontrolled release into the air. Use appropriate engineering controls. Use only in well-ventilated areas. Use the smallest amount necessary.
Wear appropriate PPE.
Inspect containers for damage or leaks before handling. Open containers slowly and carefully. Dispense carefully and keep containers closed when not in use.
Clean up any spills or dust buildup promptly and safely.
Report leaks, spills or ventilation failures immediately.
Store away from incompatible materials and in a cool, dry, well-ventilated area and out of direct sunlight.

## Slide 186: Aspiration Hazard
Aspiration occurs when a liquid or solid enters the trachea (windpipe) and the lungs. The product can enter or be aspirated directly through the nose or mouth, or it may enter indirectly as a result of vomiting
  Examples: petroleum distillates (e.g., hexane, octane, gasoline), aromatic hydrocarbons (e.g., kerosene), pine oils, turpentine, paint thinners, and mineral oils.
NOTE: The impacts of aspiration hazards can be delayed so if an exposure if suspected, prompt medical assessment must be sought so preventive treatment can begin.

## Slide 187: Aspiration Hazard
Hazard category | Pictogram | Signal word | Hazard statement
1 | Health hazard | Danger | May be fatal if swallowed and enters airways

## Slide 188: Aspiration Hazard
Key Precautions
Prevent uncontrolled release into the air. Use appropriate engineering controls. Use only in well-ventilated areas. Use the smallest amount necessary.
Inspect containers for damage or leaks before handling. Open containers slowly and carefully. Dispense carefully and keep containers closed when not in use.
Store away from incompatible materials and in a cool, dry, well-ventilated area and out of direct sunlight.
In the event of exposure, move to fresh air. Alert others of potential exposure.
Do not induce vomiting as this action is an aspiration hazard.
Effects of exposure may be delayed by up to 24 hours. Get medical attention after a known exposure even if no symptoms are felt.

## Slide 189: Biohazardous Infectious Materials
It includes any microorganism, nucleic acid, or protein that may cause an infection in humans or animals.
Understand all of the hazards associated with the product, and how to use it safely. Read the label and SDS for more information.
Hazard category | Pictogram | Signal word | Hazard statement
1 | Biohazardous infectious materials | Danger | (Wording that describes the nature of the hazard)

## Slide 190: Health Hazards Not Otherwise Classified
The label and SDS will list the hazards associated with the product. Be sure to read the label and SDS.
The pictogram, signal word, and hazard statements will be chosen to reflect the hazard present.
Hazard category | Pictogram | Signal word | Hazard statement
1 | As applicable | Danger | Applicable wording for the hazard.

## Slide 191: Hazardous to the Aquatic Environment (short-term) (not mandatory)
This class covers the acute (short term) effects on various aquatic life forms such as fish, crustaceans, algae and aquatic plants.

## Slide 192: Hazardous to the Aquatic Environment (short-term) (not mandatory)
Hazard category | Pictogram | Signal word | Hazard statement
1 | Environment | Warning | Very toxic to aquatic life
2 | No pictogram | No signal word | Toxic to aquatic life
3 | No pictogram | No signal word | Harmful to aquatic life

## Slide 193: Hazardous to the Aquatic Environment (short-term) (not mandatory)
Key Precautions
Have spill control procedures and equipment. Contain spill quickly by diking with spill socks or suitable absorbent material. Do not leave spill site unattended.
Prevent product from contaminating ground water, surface waters and sewer system. Protect floor drains, cover opening to sewer if able to do so.
Store product in a secure, dry, well-ventilated location. Storage area should have sills and prevent leaks and spills from escaping to sewers.
Use secondary containment for containers such as drip trays to contain leaks or spills. Empty trays regularly to avoid overflow. Monitor use of product. Unexpected increased use may indicate leakage.
Report leaks and spills.

## Slide 194: Hazardous to the Aquatic Environment (long-term) (not mandatory)
Covers products that can have long-term negative impacts on the environment (chronic effects)
Bioaccumulation refers to the accumulation of a substance in aquatic organisms. Bioaccumulation may or may not have a toxic effect on some organisms but it is a concern because when other organisms eat smaller organisms, they accumulate more of the substance.
Degradation of the substance refers to whether the product breaks down quickly or whether it is persistent and remains in the environment.
Examples of effects could include reduced spawning, genetic problems in offspring, and behavioural changes.

## Slide 195: Hazardous to the Aquatic Environment (long-term) (not mandatory)
Hazard category | Pictogram | Signal word | Hazard statement
1 | Environment | Warning | Very toxic to aquatic life with long lasting effects
2 | Environment | No signal word | Toxic to aquatic life with long lasting effects
3 | No pictogram | No signal word | Harmful to aquatic life with long lasting effects
4 | No pictogram | No signal word | May cause long lasting harmful effects to aquatic life

## Slide 196: Hazardous to the Aquatic Environment (long-term) (not mandatory)
Key Precautions
Have spill control procedures and equipment ready. Contain spill quickly by diking with spill socks or suitable absorbent material. Do not leave spill site unattended.
Prevent chemical from contaminating ground water, surface waters and sewer system. Protect floor drains, cover opening to sewer if able to do so.
Store substance in a secure, dry, well-ventilated location. Storage area should have sills and prevent leaks and spills from escaping to sewers.
Use secondary containment for containers such as drip trays to contain leaks or spills. Empty trays regularly to avoid overflow. Monitor use of product. Unexpected increased use may indicate leakage.
Isolate loading and unloading areas from surface water drainage systems. If not possible, protect drains using covers, sandbags, etc.
Report leaks and spills.

## Slide 197: Hazardous to the Ozone Layer (not mandatory)
Ozone-depleting substances (ODS) are gases which damage the ozone layer in the upper atmosphere.
Common examples include refrigeration and air-conditioning equipment, aerosols, solvents, foam blowing agents, firefighting fluids, and high voltage switchgear.

## Slide 198: Hazardous to the Ozone Layer (not mandatory)
Hazard category | Pictogram | Signal word | Hazard statement
1 | Exclamation mark | Warning | Harms public health and the environment by destroying ozone in the upper atmosphere

## Slide 199: Hazardous to the Ozone Layer (not mandatory)
Key Precautions
Use the smallest amount necessary. Only use the permitted refrigerants when servicing.
Ensure that ODS are properly recovered when servicing, maintaining and decommissioning equipment. Ensure that only those properly trained and qualified perform service on the equipment.
Consider automatic leak detection systems for larger quantities.
Regularly inspect and maintain equipment and storage area and for signs of leakage or damage. Repair as soon as possible. Follow up to ensure that leaks have been securely contained.
Maintain records – quantities used, amounts lost, added or recovered, dates for inspection/maintenance etc.
Ensure that systems containing these products are properly labelled.

## Slide 200: Workplace Specific Training

## Slide 201: Site-Specific WHMIS Program
According to Saskatchewan legislation your employer must:
Inform you about all hazard information concerning the specific hazardous products in your workplace
Educate and train you to be able to apply this hazard information to protect your health and safety
Consult with your OHC about this education and training program
Periodically test your knowledge in WHMIS
Annually review WHMIS education and training program with the OHC or when changes occur in workplace conditions and/or hazard information concerning hazardous products

## Slide 202: Site-Specific WHMIS Program
This means you can expect to see in your site-specific WHMIS program at your workplace:
  An inventory of all hazardous products in your worksite
  Education and training regarding the hazardous products specific to your workplace
  Documented procedure(s) to be followed in case of an emergency with a hazardous product
  A written test or sign-off of practical demonstration of your site-specific WHMIS knowledge performed on a periodic basis
  Appropriate SDSs be readily available to you by electronic and/or print at all times

## Slide 203: Workplace Specific Training
What are the hazards of the product?
  Understand the label and SDS
How are you protected from those hazards?
  Understand of the controls used in the workplace.
What do you do in case of an emergency?
  Procedures to follow in the event of a spill, release, or fire; or if health effects are noticed.
Where can you get hazard information?
  Know how to get the SDS (either by the binder/location, or by accessing via a computer).

## Slide 204: ACTIVITY: Workplace-Specific Worksheet

## Slide 205: As a worker, can you answer these four questions about every product you work with or may be exposed to?
  What are the hazards of the product?
  How are you protected from those hazards?
  What do you do in case of an emergency?
  Where can you get hazard information?